# PID
## How It works

Most robots use a form of a control loop to move efficiently and accurately rather than using a proportional statement at max speed because that can overshoot by large amounts. So we opted for one of the most common forms of a control loop, The PID loop. PID standing for Proportional Integral Derivative. The proportional element is what defines how fast it will move depending on the difference between the target and its current position which we call error in this scenario. So the robot moves at a speed which is the product of the error and the proportional element (also called KP). Next is the integral element which is a sum of all the previous loop’s errors. This element controls the steady acceleration so that when the robot is almost at it’s destination but not quite this can close the gap that the proportional element usually doesn’t. Finally the derivative element which is used to predict the future error and correct for it to prevent overshooting your final destination. All of these elements are put together in a formula with constants so that you can tune the PID loop to fit your robot.
## Our Implementation
The following code snippets are from our PID turning and driving functions which can be found in full at the end of this section. First we started out by defining our variables (shown on the left) that are used in the PID loop itself. The first three variables are the constants that are mentioned above (Kp, Ki, and Kd). The next variable with the name d is simply the unsigned error and only exists for neatness. The variable speed is used to store the result from the PID equation to be used in the statements that tell the motors to move. The previous error variable is used for storing the error from the previous loop to be used in the integral element of the equation. Next are the variables that will be multiplied by the first three constants above then added to generate the speed to be used for the motors. Error is set to a value of 361 due to the condition for the while loop below requiring a value of greater than one to continue looping so I picked the arbitrary value of 361. The following code snippets shown in images are inside a while loop that looks like what is shown on the right. For the actual PID calculation we had to figure out a way of modeling the PID equation because it’s calculating most concepts from calculus exactly due to computers not being able to calculate to an infinite degree so instead we sidestep this problem by running the calculations for an instant and then looping that calculation which takes a very small amount of time. This allows us to approximate or get very close to the real speed it should be moving. After putting all this together we were able to create this little snippet of code which would give us the speed we should be moving at by tuning a couple of constants so we could have smooth driving and turning with very small error. Although after testing this we faced a very large problem. When we began tuning the integral constant the robot would overshoot by large amounts. We realized this was a problem where the PID loop would integrate the error at the start of the loop when the error was at its largest causing the integral to grow to very large amounts even with a very small integral constant. So we did some research and found what is called a “Windup Mechanism” where we do not integrate until the error is below a certain threshold so we take care of the steady-state error instead of overshooting.
### Turn Specific PID
For the different applications we had for PID control we had to slightly change our algorithm to reflect the application required. Turning using PID control was especially difficult. Finding the difference between to angles proves harder than I first imagined. It’s not as simple as just lateral movement where you take the difference between the target wheel positions and the current wheel positions. So I implemented this solution to finding the angle between the
### Drive Specific PID
One of the major issues we faced that was specific to our lateral movement PID function was the robot not driving entirely straight.

# Usability

## Battery Indicator
If the battery capacity is above 75% then the green light is on, if it is greater than 50% but less than 75% than the yellow light is on, or if it is 50% or lower then the red light is on.
## Base Motor Heat Readouts
The heat of all four motors is averaged then printed out to the controllers.

# User Control

## Tank Control Toggle
We have a toggle button that toggles between driver control and tank control.

## Vision Sensor
When we had the what we called the back-chute mechanism we decided it would be beneficial to sort balls automatically using a vision sensor I was very excited to jump on this opportunity to figure out how the vision sensor works and how we can utilize it to sort balls. So the first step was learning how the vision sensor recognized objects and how we can use it to sort red and blue balls for cycling towers. The vision sensor takes “snapshots” of what it can see then it attempts to find objects of matching color or signature. These signatures are set in the robot configuration section of the code. After finding these signatures it returns a list of the objects which can have attributes such as size and where it is on the snapshot.
Putting all of this together I devised an algorithm to find what ball is closest to the vision sensor to control the motors of the back-chute mechanism. First I take a snapshot for both signatures and calculate the area of the largest object found in the snapshot. I then compare the area of the red signature to the area of the blue signature. Although this will only find the largest ball that the vision sensor can see. This won’t account for how close it is to the vision sensor. In the event it sees a blue or red ball across the field it will think there is a red or blue ball in the roller train. To solve this I compare the area to a constant. If it is above the threshold then I know it is close to the vision sensor. Putting this all together I know which color ball is in the roller train. Now the final thing to make all this work is to decide which color ball to keep and which color to throw out when cycling. I had the idea to use the autonomous selection menu to determine whether you are on the red or blue alliance. Thus deciding which ball to sort out.