# PID
## How It works

Most robots use a form of a control loop to move efficiently and accurately rather than using a proportional statement at max speed because that can overshoot by large amounts. So we opted for one of the most common forms of a control loop, The PID loop. PID standing for Proportional Integral Derivative. The proportional element is what defines how fast it will move depending on the difference between the target and its current position which we call error in this scenario. So the robot moves at a speed which is the product of the error and the proportional element (also called KP). Next is the integral element which is a sum of all the previous loop’s errors. This element controls the steady acceleration so that when the robot is almost at it’s destination but not quite this can close the gap that the proportional element usually doesn’t. Finally the derivative element which is used to predict the future error and correct for it to prevent overshooting your final destination. All of these elements are put together in a formula with constants so that you can tune the PID loop to fit your robot.
## Our Implementation
The following code snippets are from our PID turning and driving functions which can be found in full at the end of this section. First we started out by defining our variables (shown on the left) that are used in the PID loop itself. The first three variables are the constants that are mentioned above (Kp, Ki, and Kd). The next variable with the name d is simply the unsigned error and only exists for neatness. The variable speed is used to store the result from the PID equation to be used in the statements that tell the motors to move. The previous error variable is used for storing the error from the previous loop to be used in the integral element of the equation. Next are the variables that will be multiplied by the first three constants above then added to generate the speed to be used for the motors. Error is set to a value of 361 due to the condition for the while loop below requiring a value of greater than one to continue looping so I picked the arbitrary value of 361. The following code snippets shown in images are inside a while loop that looks like what is shown on the right. For the actual PID calculation we had to figure out a way of modeling the PID equation because it’s calculating most concepts from calculus exactly due to computers not being able to calculate to an infinite degree so instead we sidestep this problem by running the calculations for an instant and then looping that calculation which takes a very small amount of time. This allows us to approximate or get very close to the real speed it should be moving. After putting all this together we were able to create this little snippet of code which would give us the speed we should be moving at by tuning a couple of constants so we could have smooth driving and turning with very small error. Although after testing this we faced a very large problem. When we began tuning the integral constant the robot would overshoot by large amounts. We realized this was a problem where the PID loop would integrate the error at the start of the loop when the error was at its largest causing the integral to grow to very large amounts even with a very small integral constant. So we did some research and found what is called a “Windup Mechanism” where we do not integrate until the error is below a certain threshold so we take care of the steady-state error instead of overshooting.
## How we tuned it
The Tuning is still a WIP

Implementation of PID Turning with line by line explanation of PID loops and how I implemented it.
Usability

 Battery Indicator
If the battery capacity is above 75% then the green light is on, if it is greater than 50% but less than 75% than the yellow light is on, or if it is 50% or lower then the red light is on.
Base Motor Heat Readouts
The heat of all four motors is averaged then printed out to the controllers.

User Control

Tank Control Toggle
We have a toggle button that toggles between driver control and tank control.

Vision Sensor